## Slide 1: GNNBuilder An Automated Framework for Generic Graph Neural Network Accelerator Generation, Simulation, and Optimization
Stefan Abi-Karam1,2, Cong Hao1
1Georgia Institute of Technology, 2Georgia Tech Research Institute
stefanabikaram@gatech.edu, callie.hao@ece.gatech.edu
  Sharc Lab @ Georgia Tech sharclab.ece.gatech.edu

## Slide 2
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 3
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 4: Deep Learning for Graphs
What “Deep Learning for Graphs” applications benefit most from hardware acceleration?

## Slide 5: Deep Learning for Graphs
High Energy Physics!
Point Cloud Processing

## Slide 6: Deep Learning for Graphs
High Energy Physics!
Point Cloud Processing
Benefit from hardware acceleration for real-time inference!

## Slide 7
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 8: Graph Neural Networks (GNNs)
Graph Convolutions
Node-Level Embedding *
Pool Nodes **
Graph Prediction Head
Graph-Level Embedding
* Or compute edge embeddings
** Stop here for node-level
and edge-level tasks
1
3
4
2
5

## Slide 9: Graph Neural Networks (GNNs)
Graph Convolutions
Node-Level Embedding *
Pool Nodes **
Graph Prediction Head
Graph-Level Embedding
* Or compute edge embeddings
** Stop here for node-level
and edge-level tasks
1
3
4
2
5
This part is the challenge!

## Slide 10
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 11: GNN Hardware Acceleration Landscape
EnGN
HyGCN
AWB-GCN
GRIP
Auten et al.
Zhang et al.
Rubik
GCNAX
GraphACT
BoostGCN
I-GCN
✅ Hardware Acceleration
❌ General Computation
❌ End-To-End Automation
✅ Hardware Acceleration
✅ General Computation
❌ End-To-End Automation
GenGNN
✅ Hardware Acceleration
✅ General GNN Computation
✅ End-To-End Automation
FlowGNN
HPCA 2023
GNNBuilder
FPL 2023

## Slide 12: Design Workflow
Logic Synthesis
Physical Synthesis
  C/C++
  RTL (Verilog)
  Netlist
High-Level
Synthesis
  Bitstream
  FPGA
Software Models are Always Changing
!
Hardware Design is Complex, Slow, and Requires Expert Knowledge
Platforms are Varied and Heterogeneous
!
!
!

## Slide 13: GNNBuilder Overview
Generic Compute: wide range of GNN model support
Architecture: Parameterizable SW and HW model architecture
Design Space Exploration: ML-based DSE models
Performance Results: Better performance against CPU and GPU
Framework API: Open-source Python API with end-to-end workflow
Extensibility: Interoperability with PyTorch and extendable by anyone

## Slide 14
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 15
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Hardware
Compiler
Software

## Slide 16: “SpMM is Not All You Need”
Non-Sum Aggregation
PNA + GraphSAGE
Anisotropic Message Passing
Graph Attention Networks
Edge Embeddings
Almost all other cases…
GCN + GIN+ GraphSAGE
“SpMM is All You Need”
Sum-Multiply Reductions

## Slide 17: “SpMM is Not All You Need”
“SpMM is All You Need”
EnGN
HyGCN
AWB-GCN
GRIP
Auten et al.
Zhang et al.
Rubik
GCNAX
GraphACT
BoostGCN
I-GCN
✅ Hardware Acceleration
❌ General Computation
✅ Hardware Acceleration
✅ General Computation
FlowGNN
GNNBuilder

## Slide 18: Generic Compute

## Slide 19: Generic Compute

## Slide 20
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Hardware
Compiler
Software

## Slide 21: Model Architecture
Support a parameterized model architecture for node-level and graph-level tasks.

## Slide 22: Model Architecture
Fully parameterized GNN model using PyTorch Geometric.
Notes: The model behaves as a native PyTorch “nn.Module” and can be trained + used in deep learning workflows.

## Slide 23
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Hardware
Compiler
Software

## Slide 24: Hardware Architecture
We use an explicit message passing hardware kernel architecture for each graph convolution.

## Slide 25: Hardware Architecture
The entire GNN Backbone is an “HLS DATAFLOW” region allowing for higher data throughput between layers without stalling.
GNN Backbone
Graph Conv. Layer 1
Graph Conv. Layer 2
Graph Conv. Layer 3
Graph Conv. Layer 4
#pragma HLS DATAFLOW

## Slide 26: Graph Representation in Memory
We support COO (edge list) format for graph input.
We process the graph to create a degree table and neighbor table.
All this processing is done once on the device during inference.
1 | 2 | 4 | 4
2 | 3 | 3 | 2
0 | 2 | 2 | 0
1 | 1 | 0 | 2
COO Edge List
From:
To:
Degree Tables
In-Degree:
Out-Degree:
n1
n2
n3
n4
Neighbor Offset Table
Neighbor Table
Compute
Compute
1 | 4 | 2 | 4
0 | 0 | 2 | 4

## Slide 27
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Hardware
Compiler
Software

## Slide 28
GNNBuilder comes with a modular C++ HLS header library for GNN compute!
HLS Implementation
Notes: GNNBuilder comes with a modular C++ HLS header library for GNN compute!
This is where all the HW components are implemented for HLS.
Components of the same type (layers, aggregations, …) follow a common template and signature interface.
Open Source: anyone can look and use!
Each PyTorch Geometric layer has an equivalent hardware kernel:
GCN, GIN, GraphSAGE, PNA, …
Extra building blocks used throughout:
Linear Layers
Activations
Aggregations
Degree + Neighbor Table Processing

## Slide 29: HLS Implementation
Break down key details of a GCN convolution layer.
Note how model parameters are passed down to the hardware.

## Slide 30: HLS Implementation
Used for static array / memory sizing.
Set by user at design time based on dataset / workload.

## Slide 31: HLS Implementation
Used for static array / memory sizing.
Used for passing in “ap_fixed” typedef as user-defined fixed-point datatype.
Set by user at design time based on task accuracy tradeoff.

## Slide 32: HLS Implementation
Used for static array / memory sizing.
Used for passing in “ap_fixed” typedef.
Used for “#pragma HLS tripcount” to improve latency estimation.
Estimated from dataset / workload at design time.

## Slide 33: HLS Implementation
Used for static array / memory sizing.
Used for passing in “ap_fixed” typedef.
Used for “#pragma HLS tripcount” to improve latency estimation.
Used to parallelize intra-layer operations such as node transformations.
Set by the user at design time based on perf. requirements and DSE exploration.

## Slide 34: HLS Implementation
Used for static array / memory sizing.
Used for passing in “ap_fixed” typedef.
Used for “#pragma HLS tripcount” to improve latency estimation.
Used to parallelize intra-layer operations such as node transformations.
More details in the code repo. and documentation.

## Slide 35
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Hardware
Compiler
Software

## Slide 36: Compiler and Code Generation
GNNBuilder implements a template-based compiler that lowers PyTorch models, down to a structured model IR, and then down to HLS C++ source code.

## Slide 37: Compiler and Code Generation
Agg. Config.
Agg. Config.
Skip Conn. Config.
Activation Config.
Linear Layer Config.
GNN Layer 0 Config.
GNN Layer 1 Config.
GNN Layer n Config.
Skip Conn. Config.
Activation Config.
We extract model and hardware architecture logic into individual compiler template components.
GNN Backbone
Config.
GNN Layer Template
Buffer Indexing Template
GNN Backbone
Dataflow Template
MLP Head
Config.
Global Pooling Config.
Graph Loading Template
Top Level Kernel Template
User Model
Complete Accelerator HLS C++ Source
GNNBuilder Compiler

## Slide 38: Extra Features
User specified fixed-point data type for features and weights
  Uses ap_fixed format Xilinx HLS library
  Also uses hls::math library
Auto build and run of C++ testbench using Clang
  Can export PyTorch Geometric dataset to testbench files
  Can use testbench as a correct model to explore quantization loss
Auto synthesis using Vitis HLS
  Runs synthesis flow for a user-specified device and clock speed
  Extracts synthesis results: latency + resource usage
Auto deploy to FPGA with host code (work in progress)
  Run Vitis + Vivado build flow to generate .xclbin
  Generate OpenCL host code to evaluate dataset (like testbench)
  Looking into using XRT support in the PYNQ library to keep everything in Python

## Slide 39
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 40: Design Space Exploration
Predicting Latency and Resource Usage
Analytical Model
ML-Based Model
Success!
Generalizes Across Accelerator Configs.
Complete Failure!
Too Much Complexity
Config.
Notes: Analytical Model
Look at HLS code and translate to Python model to calculate a rough estimate of clock cycles and resources.
Complete Failure!
Too much complexity in HLS synth + mapping and dynamic runtime workload make it hard to do this accurately.
Fitted Model
Use a random forest model and fit to a dataset of 400 randomly sampled model designs + configurations.
The ML model acts as a “smart interpolator” of the sparsely sampled configuration space.
Success!
This approach has good cross-validation error even with a very small sampled dataset of designs.

## Slide 41: Design Space Exploration
MAPE: Mean Absolute Percent Error
Notes: We achieve accurate predictions for latency and BRAM usage with low error that generalize to unfitted designs.

## Slide 42: Design Space Exploration
Single DSE Model - 1.7 ms.
Single HLS Synthesis - 9.5 min.

## Slide 43
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 44
Accelerator Performance
CPU: Intel Xeon Gold 6226R
GPU: Nvidia RTX A6000
FPGA: Xilinx Alveo U280 @ 300 MHz.
We use a batch_size=1
across all evaluations for
real-time inference applications.

## Slide 45
We achieve consistent speedups overs CPU and GPU implementations!
Accelerator Performance

## Slide 46
Resource usage is dominated by on-chip memory (BRAM / URAM)
Accelerator Performance

## Slide 47
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 48: Framework API
Notes: Both accelerator design generation and build flows are accessed via the GNNBuilder Python API.

## Slide 49
Minimum working example to generate, testbench, and synth a GNN accelerator.

## Slide 50
Minimum working example to generate, testbench, and synth a GNN accelerator.
Specify Dataset / Workload
Specific GNN PyTorch Model
(can be used for training)
(or load a pre-trained model)
Characterize Dataset / Workload Graph Properties
Specify GNNBuilder Accelerator Project
(Define build path, device, tools, and fixed-point spec.)
Compile Down to HLS Design, Testbench, and Build Files
Call Tools to Run Hardware Testbench, Synthesis, and Implementation
Import GNNBuilder

## Slide 51
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 52: Limitations
GNNBuilder ⇒ 7x speedup vs. FlowGNN ⇒ up to 400x speedup
No Node-Level Parallelism in GNNBuilder
  Each node is evaluated sequentially, nodes are not processed in parallel.
GNNBuilder
FlowGNN

## Slide 53: Limitations
GNNBuilder ⇒ 7x speedup vs. FlowGNN ⇒ up to 400x speedup
No Node-Level Parallelism in GNNBuilder
  Each node is evaluated sequentially, nodes are not processed in parallel.
GNNBuilder
FlowGNN
Adapt dataflow pipelining and parallelism from previous GNN accelerator publications.
GenGNN and FlowGNN

## Slide 54
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 55: Ongoing Work
Large Graph Support via Efficient Off-Chip HBM Access
Irregular unknown memory access patterns at runtime
Automated XRT and PYNQ On-Device Deployment and Evaluation
Expand Support for Novel GNN and NN Features
GAT, SimpleConv, Graph Sampling, Embedding Lookup Layers, Complex Edge Convs, …
Multi-Tiered Accelerator Evaluation API
Fitted Models → LightningSim Co-Simulation → Vitis HW Emulation → On-Device Evaluation
Application Demos and Deployment
High Energy Physics Triggers and Reconstruction, Real Time Point Cloud Processing, …

## Slide 56
GNNBuilder
Architecture
Generic Compute
Design Space Exploration
Performance Results
Framework API
Background
  DL for Graphs
  GNNs
  Accelerators
GNNBuilder
  Generic Compute
  Architecture
  Design Space Exploration
  Performance Results
  Framework API
Limitations
Ongoing Work
Documentation and Open Source

## Slide 57: Source Code + Documentation + Setup
github.com/sharc-lab/gnn-builder
sharc-lab.github.io/gnn-builder/
Source Code
Documentation + Tutorials
pip install git+https://github.com/sharc-lab/gnn-builder.git
🚧
conda install --channel https://sharc-lab.github.io/gnn-builder/repo gnn-builder
🚧

## Slide 58: How to Add a New Graph Convolution Layer
Clone the repo…
Add HW kernel to header library…
Add associated layer wrapper to Python library…
Add the relevant compiler template unit…
Run testbench and synth…
Submit pull request…
See documentation for detailed walkthroughs and tutorials.

## Slide 59: GNNBuilder An Automated Framework for Generic Graph Neural Network Accelerator Generation, Simulation, and Optimization
Interested in perusing academia…
Stefan Abi-Karam
stefanabikaram@gatech.edu
SHARC Lab @ Georgia Tech
sharclab.ece.gatech.edu
TMPO / CIPHER
Georgia Tech Research Institute

## Slide 60
Undergraduate Student Mentoring
Raised $60K Internal Research Funding
New Research Direction
External Collaborations
Stefan Abi-Karam
Research Faculty
Ph.D. Student
stefanabikaram@gatech.edu
stefanabikaram.com

## Slide 61: Sharc Lab @ Georgia Tech
Prof. Callie Hao

## Slide 62: Deep Learning on Graphs
Benefits From Inference Acceleration
Doesn’t Need Inference Acceleration
Physics Modeling
Scene Graph Understanding
Source Code Analysis
NLP
HW/SW Co-Design
Smart EDA Tools
Hardware Security
Weather Forecasting
Social Network Analysis
Recommender Systems
Drug Discovery
Fraud Detection
…
…
Many more…
High Energy Physics!
Point Cloud Processing

## Slide 63
Accelerator Performance
We use a batch size of 1 across all evaluations.
For real time inference applications such as high energy physics triggers or autonomous vehicles, this is a reasonable assumption to make. We are unable to batch data in these cases.
If batching is needed, multiple graphs can be treated as one disconnected graph.
All benchmarks share the following model parameters:
GNN Hidden Dim | 128
GNN Hidden Layers | 6
GNN Output Dim | 64
GNN Activation | ReLU
GNN Skip Connections | True
Global Pooling | [add, mean, max]
MLP Head Input Dim | 64 x 3
MLP Hidden Dim | 64
MLP Hidden Layers | 4
MLP Activation | ReLU

## Slide 64
Evaluated Parallelism Factors
Evaluated Fixed Point Types
Accelerator Performance
Model Type | Input Parallelism | Hidden Parallelism | Output Parallelism
FPGA-Parallel: GCN, SAGE, GIN | gnn_p_in=1, p_in=8 | gnn_p_hidden=16, p_hidden=8 | gnn_p_out=8, p_out=1
FPGA-Parallel: PNA | gnn_p_in=1, p_in=8 | gnn_p_hidden=8 | gnn_p_out=8, p_out=1
FPGA-Base | 1 | 1 | 1
Model Type | Fixed-Point Type
FPGA-Parallel: GCN, SAGE, GIN | ap_fixed<16, 10>
FPGA-Parallel: PNA | ap_fixed<16, 10>
FPGA-Base | ap_fixed<16, 32>
CPU: Intel Xeon Gold 6226R
GPU: Nvidia RTX A6000
FPGA: Xilinx Alveo U280 @ 300 MHz.

## Slide 65
Accelerator Performance
We achieve consistent speedups overs CPU and GPU implementations!
Based on results from FlowGNN we can roughly estimate power efficiency.
Approximate FPGA power: ~30W
Approximate GPU power: ~70W
This results in a ~2.33x approximate power efficiency margin for the same throughput between devices.
Memory efficiency has yet to be profiled.
This is under the current work to support large graphs, HBM support, and graph sampling.

## Slide 66: Compiler and Code Generation
We extract model and hardware architecture logic into individual compiler template components.
Figure out which double buffer or input / output buffer to use for each layer.
Mapping PyTorch layers and parameters to hardware kernels.